Public contract entited:

Delivery of an oxygen atom source, low-temperature and high-temperature effusion cells for the MBE system (OP JAK - FerrMion)

The subject of the procurement procedure is the supply of an oxygen atom source, low-temperature and high-temperature effusion cells* (Molecular Beam Epitaxy).

* The MBE system will be used for the preparation of hybrid nanostructures based on fullerenes and ferroic nanoparticles. The MBE system will consist of a large-volume vacuum chamber with a connected system of active elements, a sample manipulator, a thickness monitor and a system for linear sample transfer.

1) Oxygen atom beam source

The oxygen atom source will be used in the project for a dual purpose: cleaning the surface of the substrates before deposition of materials from carbon impurities, and formation of the oxide layer. In combination with the metals evaporated from other sources (to form ferroics), the oxygen beam will allow to grow various types of films. The application requires UHV compatibility and accurate oxygen content control. The device will be mounted on the bottom of the MBE chamber so that the oxygen beam is directed towards the center of the chamber onto the substrates.

The contracting authority sets the following minimum technical conditions:

| Subject | Parameter / Required technical and functional properties, value | The specific parameters of the offered solution or the supplier meets the conditions YES / NO | Offered solution - manufacturer, exact type leading to identification (or web link) |
| --- | --- | --- | --- |
| Oxygen atom beam source | UHV compatible |  |  |
|  | Mounting flange DN35CF-DN40CF (2.75" OD) or DN63CF (4.50” OD) |  |  |
|  | Internal water-cooling |  |  |
|  | Integrated thermocouple |  |  |
|  | In vacuum length up to 200 mm |  |  |
|  | UHV leak valve CN16CF |  |  |
|  | Operating temperature for dissociation about 1800 °C |  |  |
|  | Compatible power supply + PID controller for 19” rack with cables |  |  |
|  | Warranty period min. 12 months |  |  |

Note: the supplier must fill in all fields highlighted in yellow

2) Low temperature effusion cell

A low-temperature effusion cell is required for the controlled evaporation of fullerene molecules onto substrates. The cell will be mounted on the bottom of the MBE vacuum chamber facing the substrate located in the center of the chamber. The temperature range must be suitable for the operating mode of vaporization of fullerene molecules. In conjunction with electron guns designed for the evaporation of metals, it will enable the synthesis of thin hybrid ferroics.

​

The contracting authority sets the following minimum technical conditions:

| Subject | Parameter / Required technical and functional properties, value | The specific parameters of the offered solution or the supplier meets the conditions YES / NO | Offered solution - manufacturer, exact type leading to identification (or web link) |
| --- | --- | --- | --- |
| Low temperature effusion cell | UHV compatible |  |  |
|  | Mounting flange DN35CF-DN40CF (2.75" OD) or DN63CF (4.50” OD) |  |  |
|  | Crucible with volume between 5 cc and 15 cc |  |  |
|  | Integrated thermocouple |  |  |
|  | Operating temperature up to 1000°C or 1100°C |  |  |
|  | Integrated water cooling |  |  |
|  | Manual shutter with rotary feedthrough |  |  |
|  | In vacuum length up to 220 mm |  |  |
|  | Compatible power supply + PID controller for 19” rack with a cable set |  |  |
|  | Warranty period min. 12 months |  |  |

Note: the supplier must fill in all fields highlighted in yellow

3) High temperature effusion cell

A high melting point effusion cell is required for the controlled evaporation of pure metals with a lower melting point. The high temperature effusion cell will be mounted on the bottom of the UHV MBE chamber directly against the substrate in the center of the chamber. A wider temperature range is required to vaporize lower melting metals that will form thin interface films of pure metals deposited on a substrate prior of hybrid ferroic films.

The contracting authority sets the following minimum technical conditions:

| Subject | Parameter / Required technical and functional properties, value | The specific parameters of the offered solution or the supplier meets the conditions YES / NO | Offered solution - manufacturer, exact type leading to identification (or web link) |
| --- | --- | --- | --- |
| High temperature effusion cell | UHV compatible |  |  |
|  | Mounting flange DN35CF-DN40CF (2.75" OD) or DN63CF (4.50” OD) |  |  |
|  | Crucible volume between 1 cc and 2 cc |  |  |
|  | Integrated thermocouple |  |  |
|  | Operating max temperature between 1700°C and 1900°C |  |  |
|  | Integrated water cooling |  |  |
|  | Manual shutter with rotary feedthrough |  |  |
|  | In vacuum length up to 220 mm |  |  |
|  | Compatible power supply + PID controller for 19” rack with a cable set |  |  |
|  | Warranty period min. 12 months |  |  |

Note: the supplier must fill in all fields highlighted in yellow

4) Supplier offer:

| Subject | Total offer price in EUR without VAT |
| --- | --- |
| 1) Oxygen atom beam source (1 pc) | …….. EUR |
| 2) Low temperature effusion cell (1 pc) | …….. EUR |
| 3) High temperature effusion cell (1 pc) | …….. EUR |
| Packing and shipping | …….. EUR |
| Total offer price in EUR without VAT | …….. EUR |
| Estimated value of the subject of performance including transport to the headquarters (in CZK without VAT) | 1 200 000 CZK |

Note: the supplier must fill in all fields highlighted in yellow

___________________________________________

signature of an authorized person on behalf of the supplier